## Slide 1: IP-Core based ASIC & FPGA design methodology
L. Fossati ESA/ESTEC 16/09/2013

## Slide 2: Outline
Introduction
  New Design methodologies: why and what?
  ESL Development Flow
Synthesizable HDL IP-Cores
  What is an IP-Core
  Why are IP-Cores useful
  IP-Cores enabling design re-use
Hw/Sw Codesign: Behavioral SystemC IP-Cores
  Complementing IP-Cores for a modern design flow
Conclusions

## Slide 3: Introduction New Design Methods: Why?
Evolution in Time
Standard Instruction-Set
Standard
Components
Discrete
Components
Module in a Chip
First VLSI
Circuits
Systems-on-Chip
Standard Devices
Standard Design

## Slide 4: Introduction New Design Methods: Why?
Evolution in Time
Standard Instruction-Set
Standard
Components
Discrete
Components
Module in a Chip
First VLSI
Circuits
Systems-on-Chip
Standard Devices
Standard Design
Evolution in Designs must be met by Evolutions in Design methodologies
As in the ‘90s we moved from schematics to VHDL

## Slide 5: Introduction New Design Methods: Why?
1.5MGates
~20 IP-Cores (Astrium, ESA, AG)
Astrium’s SCOC3

## Slide 6: ESL: Designing Methodologies
Electronic System-Level Design - definition [1]:
The utilization of appropriate abstractions in order to increase comprehension about a system, and to enhance the probability of a successful implementation of functionality in a cost-effective manner.
Set of complementary methodologies that enable embedded system design, verification, and debugging through the hardware and software implementation of custom SoC, system-on-FPGA, system-on-board, and entire multi-board systems
Main goal is to improve the productivity and quality of the complete chip deliverable, including both hardware and software…
  … but also reduce time-to-market, cost, improve re-usability
[1]: ESL Design and Verification: A Prescription for Electronic System Level Methodology, G. Martin, B. Bailey, A. Piziali
Notes: Just explain the definition, not the points

## Slide 7: Electronic System-Level Design Development Flow
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…

## Slide 8: Electronic System-Level Design Development Flow
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…
The flow starts with the algorithmic description of the desired functionality
Usually expressed with high-level languages such as Matlab, SysML, etc.
Validates the desired functionality
Acts as an executable specification all over the design

## Slide 9: Electronic System-Level Design Development Flow
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…
Starting the partitioning between hardware and software
Hardware is described using high-level non-synthesizable behavioral models (e.g. SystemC)
Various iterations are made configuring both hardware and software and moving functionalities between the two to obtain the desired tradeoff (e.g. power consumption, execution speed, silicon area, etc.)
Base HW platform:
Existing, standard cores, e.g. microprocessor, bus, etc.
Custom Hw Models:
Functionality specific to the design and to be implemented with HW accelerators
Software

## Slide 10: Electronic System-Level Design Development Flow
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…
Final system in a stable configuration
All the high-level models have been synthesized in Register Transfer Level descriptions and software compiled into object code
Ideally, at this stage prototyping on the FPGA is immediate
In case the system still doesn’t fully meet the desired requirements, further iterations of the overall flow are possible

## Slide 11: Electronic System-Level Design Development Flow
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…
IP-Cores re-use

## Slide 12: (soft) IP-Core: Definition
Intellectual Property Core – definition from Wikipedia:
In electronic design a semiconductor intellectual property core, IP core, or IP block is a reusable unit of logic, cell, or chip layout design that is the intellectual property of one party.

## Slide 13
Actually … a bit more complicated than assembling Lego bricks

## Slide 14: IP-Cores What are they?
IP-Core
Scripts
Interfaces
Functionality
Design
Test-benches
Docs
User Manual
Datasheet
Verification & Validation Report
HDL language
case OP is
when "00" => Res <= A + B;
when "10" => Res <= A and B;
when "11" => Res <= A or B;
end case;
Notes: Again, very quickly on the slide, mostly say that it is a piece of source code

## Slide 15: IP-Cores: Why - 1 Reusing Designs
Reuse in traditional engineering is part of the standard engineering process to save time and money
  IP-Cores are the Building Blocks of Large Scale Electronic Designs
IP-Cores and Standards
  Favor use of Standards by providing reference designs
  IP-Cores as de-facto standards
Designing for reuse more expensive in first instance, but huge savings when reused
  High Return on Investment
  Especially true for FPGA designs
Notes: As example of re-use in traditional engineering, consider ordering products from a catalogue, trusting it satisfies the advertised specifications
(e.g. buying isolation material, pipes, etc. when building a house)

## Slide 16: IP-Cores: Why - 2 Securing Designs
Counteract component obsolescence and discontinuity
  guarantees the availability of some key functions
  Virtually unlimited stock
Facilitates Porting the design in alternative technologies
  E.g. more advanced tech
  Providing increased performance without the need for a redesign
Promotes multiple sources
  Similar, compatible components from different providers
Notes: E.g. of PTCD and MA28140 for Obsolescence
E.g. of Atmel, with new implementation of LEON2FT: CASTOR, 90nm vs 180nm of AT697
E.g. Astrium MDPA, Atmel’s AT697
Key functions: TMTC, communication IPs, uP …

## Slide 17: IP-Cores – Why - 3 Enabling Higher Complexity Designs
n. transistors
Microns
Notes: It is founded on a paradigm which is common to all engineering disciplines: complex systems can be obtained by assembling basic components (also called building blocks).
a gap between what gates an engineer could design per day and the actual number of gates available - The challenge is to increase designer productivity to keep pace with Moore’s Law
No example of the house ad the shed

## Slide 18: High-Complexity IP-Core base designs SCOC3

## Slide 19: High-Complexity IP-Core base designs NGMP

## Slide 20: Why Licensing instead of Developing? (*)
No value add to develop internally
  Standard IP (e.g. PCI Express, USB)
  Development cost greater than licensing fee
Immediate need
  Development time exceeds “need by” date
  May be forced to compromise (e.g. features, maturity, area, power)
Can’t afford internal development
  Licensing IP most times cheaper
  Lack skills/money
Misconception
  More companies using IP -> less bugs
  How hard can it be to integrate a widely used IP?
(*) Challenges of Integrating External IP – J. Nunez, Freescale

## Slide 21: Designing for IP Reuse
Maximize Flexibility
  Configurable, parametrizable
Usage in Multiple Technologies
  Complex, configurable synthesis scripts, easy to insert/change/select technology specific elements
Comprehensive Verification Process
  Adjustable for every IP-Core configuration
Validation to a High Confidence Level
  Physical prototypes, demonstrators
Comprehensive and Clear User Documentation
  Including proper coding style and code documentation
Maintenance and Support also to be taken into account

## Slide 22: Designing for IP Reuse
Maximize Flexibility
  Configurable, parametrizable
Usage in Multiple Technologies
  Complex, configurable synthesis scripts, easy to insert/change/select technology specific elements
Comprehensive Verification Process
  Adjustable for every IP-Core configuration
Validation to a High Confidence Level
  Physical prototypes, demonstrators
Comprehensive and Clear User Documentation
  Including proper coding style and code documentation
Maintenance and Support also to be taken into account
Statically (e.g. “generics”) or at runtime (e.g. signals) to enable servicing the widest range of use cases
Need to easily support the most common technologies of the target user
Important to trust the design; re-verifying it can be expensive (if feasible)
Enables integrators to understand the design to better configure, synthesize, etc.

## Slide 23: The Importance of Interfaces
Standard Interfaces
favor IP reuse

## Slide 24: Electronic System-Level Design ESL - HW/SW co-design
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…

## Slide 25: Virtual Platform
Virtual Platform
Hardware Model
Software
Controller,
Monitor,
Performance
Analyzer,
……..
Application
Operating System
Binary Image
Runs on
Interconnection Network / BUS
Processor
Cache
Interrupt
Controller
Embedded
Memory
Memory
Controller
CAN / SpW
Interface
ESL @ ESA
Useful both during the design of a new IP-Core and for its integration

## Slide 26: Virtual Platform: definition and benefits
Virtual Platforms are not subject to the same constraints as physical implementations:
  They are “easier” to create, modify, and observe.
Enhanced modiﬁability of the models and of its parameters
Observability, controllability and not intrusive monitoring
  Performance measuring and debugging
A Virtual Platform is a software program that can fully mirror the functionality of a target SoC or board.
ESL @ ESA

## Slide 27: Hardware Modeling
Models the Base Hardware Platform
Can be performed at various abstraction levels:
ESL @ ESA

## Slide 28: SystemC and TLM
SystemC
IEEE standard, implemented as a set of C++ classes
Standard C++ compiler can be used to generate an executable specification
Addresses various levels of abstraction down to RTL
Transaction Level Modeling (TLM)
Well-established methodology for modeling complex systems
Separates communication from computation
Modules communicate with the rest of the world by performing “transactions”
  Instead of modeling every single transferred bit, “data structures” are exchanged
ESL @ ESA

## Slide 29
Current focus of ESA ESL activities is Instruction- and Cycle- accurate models
  Good trade-off among flexibility, simulation speed, and performance (speed, power consumption, area …) estimation accuracy
Models are based on SystemC and TLM libraries/methodologies
  Built on the C++ language
  Allows expressing concurrency, synchronization and timing
ESL @ ESA
Current Activities @ ESA

## Slide 30: Electronic System-Level Design Development Flow
Hw/Sw initial partitioning
Model
Refinement
Design Space Exploration
UML SySML
C/C++ AADL SystemC Matlab Simulink
Functional/Algorithmic Specification
Base HW
Platform
Custom HW models
Software
Functionality refinement
Platform tuning /optimization
Hw/Sw co-design
Base HW
Platform
Custom HW models
Software
……
Synthesis to RTL (hw)
and ASM (sw)
HDL
-
Custom HW
Behavioural
Synthesis
HDL
Base HW Platform
Instantiation after tuning
Software
SW Synthesis
BSP creation
OS Choice
Corrections
Improvements
…
Corrections
Improvements
…
SpaceStudio
SocROCKET & SystemC Models
ASSERT & TASTE
ASSERT, TASTE, SpaceStudio, Catapult C, HDL Coder …
HDL
IP Cores

## Slide 31: Conclusions
Electronic systems are becoming more and more complex
  Necessary to adopt new methodologies to be able to efficiently design them
  Grouped under the name Electronic System-Level design (ESL)
The use of hardware IP-Cores is fundamental
  Enables re-using past designs, focus on the new, ad-hoc functionality
  Other advantages as well (securing design, promoting standards, etc.)
Other elements complete the ESL development flow
  Hw/Sw codesign, high-level, behavioral synthesis, efficient specification languages, etc.
ESA is active on most of the ESL aspects
  Today we will only focus on hardware synthesizable digital and analog IP-Cores

## Slide 32: Thank You for Listening
For more information:
  Luca.Fossati@esa.int
  http://microelectronics.esa.int
  http://www.esa.int/TEC/Microelectronics/SEM6H0AMT7G_0.html