## Slide 1: TTEthernet for Space – Further Chip IP Development
Matthias Mäke-Kail, Senior Marketing & Sales Manager
Matthias.Maeke-Kail@TTTech.com
September 16, 2013

## Slide 2: TTTech’s Mission
Providing Electronic Robustness for a More Electric and Connected World
TTTech stands for reliability, robustness and safety: Time-triggered communication platforms and certifiable electronic modules enable our customers to deploy their solutions more efficiently and profitably.
Aerospace
Automotive
Industrial
Off-Highway
Page 2

## Slide 3: What They Have in Common …
Reliable Networks & Modular Safety Platforms from TTTech
Boeing 787
NASA Orion
Audi A8
Airbus A380
Page 3

## Slide 4: TTTech Group: Capabilities & Markets
Aerospace & Defense
Automotive
Off-Highway
Globally leading know-how and products for reliable embedded controls
Support/ Engineering
Safety Relevant Embedded Software
Development Tools
Hardware/ Electronics
Chip Design to Silicon
Networking incl. Physical Layer
Testing Tools
Safety/ Certification
Industrial

## Slide 5: TTEthernet: Integrated Service Delivery in a Single Ethernet Network
Ethernet (Best Effort)
IEEE 802.3 standard traffic
Best effort (IP)
Streaming (Time-Sensitive)
ARINC 664 p7
Rate-constrained
Audio/video, payload data
Sensor fusion
Synchronous (Time-Critical)
Time-triggered Ethernet – SAE AS6802 clock synchronization Real-time control with ultra-low latency
Fault-tolerance
Safety-critical systems
Cross-Industry

## Slide 6: Development of TTEthernet
2007ff: Partnership with Honeywell, development of first generation (“TTGbE”) subsequently used in MPCV/Orion program
2008: Introduction of TTEMonitoring System
2009: Announcement of Space Act Agreement with NASA
2010ff: Projects for rotorcraft and other advanced aircraft in the Americas
2011ff: Major project with leading European defense company
2011ff: Development program with European wind power market leader
Nov. 2011: Release of SAE standard AS6802
2012ff: Development of second generation, usage in automotive projects
2012-2013: Evaluation by Eurocopter
2013ff: Cooperation with chip manufacturers
2013: Start of cooperation with Astrium and European space chip IP development
2014/2015: Expected IEEE standard, announcement of partnership with leading networking specialist
Q1 2016: Release of European space graded ASIC (pending on funding)

## Slide 7: NASA MPCV and TTTech
Page 7
  "We look forward to realizing the potential of TTEthernet technology development, which provides a high bandwidth avionics databus capability supporting future technology insertion.“
  NASA statement
NASA Orion Spacecraft: TTEthernet architecture backbone from TTTech to enable missions where maintenance and repair is not an option
Page 7

## Slide 8: TTEthernet as Open Standard

## Slide 9: Synergies/Common Core
Cross-Industry

## Slide 10: Space Chip IP/Products Concept – Derived from Common Core
* Envisaged partner offering.
No export restrictions!

## Slide 11: Expected Modification of Current IP Cores for Space
Scale chip IP to reduce the size
  Number of gates
  Frame memory usage
  Static power consumption
Enable scalable frequency
  Different network speeds (10/100/1000 Mbps)
   Dynamic power consumption

## Slide 12: Targeted Rad-Tolerant/-Hard Devices
ACTEL – Microsemi
  RT ProAsic 3 – rad-tolerant
  RTAX – rad-hard
Xilinx
  Virtex 4 QV – rad-tolerant
  Virtex 5 QV – rad-hard
ASIC
  HIREC
  IMEC
  Atmel
  …
The TTEthernet chip IP cores have to fit into these candidate devices/processes.
We offer project deliveries, these are not off-the-shelf solutions or ESA IP Cores, yet.

## Slide 13: Space End-System Variants
Variant 1: TTE-End System Space
  OSI Layer 2, 3, 4 (IP/UDP)
  For critical traffic
  Full active synchronization
Variant 2: TTE-End System Pluto
  OSI Layer 2 (TTEthernet MAC)
  Passive synchronization
  Affordable solution for non-critical sensors and actuators

## Slide 14: TTE-End System Space (I)
Interfacing with High-Performance CPUs
  TTEthernet MAC
  UDP/IP Network Stack
  Synchronization Master
Additional IP blocks
    PCI(e) Interface
  DMA Controller
  IRQ Controller
  PHY Management

## Slide 15: TTE-End System Space (II)
Description | Value
Number of Ports | 2 / 3
Speed | 10 / 100 / 1000 Mbps
Frame Memory | 1 Mbit
Host Interface | AHB / AXI / SPI / PCI
Traffic Classes | TT / RC / BE
Number of Sub-Schedules | 8
Number of Virtual Links Tx | 64
Number of Virtual Links Rx | 128
Sync Role | Master / Slave

## Slide 16: TTE-End System Pluto (I)
Planned Smart Sensor/Actuator Device
  Very Small Chip IP
  TTEthernet MAC
  Simple Host Interface AHB / AXI / SPI
  System-on-a-Chip Solution with CPU + TTEthernet IP in one FPGA

## Slide 17: TTE-End System Pluto (II)
Description | Value
Number of Ports | 1 / 2
Frame Memory | 100 kbit
Host Interface | AHB / AXI / SPI
Traffic Classes | TT / RC / BE
Number of Sub-Schedules | 2
Number of Virtual Links Tx | 16
Number of Virtual Links Rx | 32
Speed | 10 / 100 Mbps
Sync Role | Client
Fits into a small radiation tolerant/hard FPGA.

## Slide 18: IP for Space TTE-Switch
High Integrity Switch
Switch Controller COM
Switch Controller MON
End System
  For the connection of the CPU to the switch controller
CPU
  Management &
  Diagnostics
For Use in ASIC

## Slide 19: Space Product Roadmap
AVAILABLE
UNDER DEVELOPMENT
ENVISAGED
2012 2013 2014 2015 2016
Time
TTEthernet Space IP Variants
“Pluto” Space IP
For rad-tolerant/hard FPGA
PT
Prototype
PS
Preseries
SR
Series
EOL
End of Life
PT
2x 10/100 Mbps (small footprint IP)
NIC Space IP
SR
PT
2x 10/100/1000 Mbps MAC
Switch Space IP
SR
PT
12x 10/100/1000 Mbps
Switch/End System ASIC
Rad-hard ASIC
2x 10/100/1000Mbps End System
6x 10/100Mbps + 6x 10/100/1000Mbps
Management CPU
RGMII Interface
SR
PT
SR
PT
SR
Third Party Combined End System ASIC
Rad-hard ASIC
Leon CPU
2x 10/100/1000 Mbps End System
Legacy Interfaces e.g. SpaceFibre, Serial, ...
SR
PT
Looking for Funding

## Slide 20: Summary of Space Projects
MPCV Crew Module (Chip IP to Honeywell, Services and Test Equipment to NASA and LMCO), Space Act Agreement with NASA
MPCV Service Module (ESA, Astrium-ST)
Next Launcher / Avionics-X (CNES / ESA)
OBC-SA Demonstrator (DLR)
TRP for Building Blocks for Deterministic Ethernet (ESA ITT 7594) – with Astrium-ST
Launcher Avionics Studies (JAXA)