## Slide 1: Experience in Developing SpaceWire and SpaceFibre IP Cores
Steve Parkes, Chris McClements
University of Dundee
Albert Ferrer Florit, Alberto Gonzalez Villafranca
STAR-Dundee Ltd

## Slide 2: VHDL IP Cores
University of Dundee and STAR-Dundee
  Developed several widely used VHDL IP Cores
SpaceWire
  CODEC (ESA-b)
  Router
  RMAP Target
  RMAP Initiator
SpaceFibre CODEC
Many others including
  I2C, UART, SPI, CAN, EDAC, …
  AHB Switch Matrix
  3 Gsamples/s FFT processor (300 GOPS)
Information from www.star-dundee.com

## Slide 3: Atmel AT6981 Castor Architecture
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 4: Atmel AT6981 Castor SpaceWire
SpW
Router
SpaceWire
Configuration Registers
SpW Engine
SpW Engine
SpW Engine
Switch
Matrix
Internal RAM 1
Internal RAM 2
CAN
CAN
Mil Std 1553
SPARC V8
I-Cache
Debug Port
Internal RAM 3
Mil Std 1553
External Memory Interface:
PROM, SRAM, SDRAM, DDRx
Debug SpW
RMAP/PnP Bus
APB Bridge
Internal RAM 4
D-Cache
Ethernet
Ethernet
Peripheral
Peripheral
Interfaces

## Slide 5: Atmel AT6981 Castor SpaceWire
SpW
Router
RMAP Target
DMA Channel (x3)
RMAP Initiator
DMA Channel (x3)
DMA Channel (x3)
Protocol
Multiplexer
AHB
Interface
SpaceWire Engine 2
SpaceWire Engine 3
SpaceWire Engine 1
AHB
SpaceWire

## Slide 6: Standards
Why have a standard?
Makes the specification process simpler
  Rather than specifying complete protocol
  Can refer to existing standard
Reduces effort on
  Requirements
  Specification
  Architectural Design
  Validation
With standards plus validated IP cores
  Entire design risk is removed
  Standard chips & boards etc.
Reduces risk, cost, development time,…

## Slide 7: IP Core Development Process
IP Core Development Process
  Requirements
  Specification
  Architectural Design
  Functional Specification
  Detailed Design
  Implementation
  Test
  Verification
  Validation

## Slide 8: IP Core Development Process
Why is the waterfall or V-model used?
Works well if you have a clear idea of
  What is needed
  Technologies to be used
Often when developing a new standard
  We don’t quite know what we want
  We don’t quite know what we can do

## Slide 9: Waterfall Life Cycle
Requirements
Gathering
Analysis
Design
Implementation
& Testing
Integration
& System Test
Maintenance
Installation

## Slide 10: Incremental Delivery Life Cycle
Requirements
Gathering
Analysis
Design
Implementation
& Testing
Integration
& System Test
Maintenance
Installation
Implementation
& Testing
Integration
& System Test
Maintenance
Installation
Part 1
Part 2

## Slide 11: Evolutionary Life Cycle
Requirements
Analysis
Design
Implementation
Integration
Maintenance
Installation
Requirements
Analysis
Design
Implementation
Integration
Maintenance
Installation
User
Feedback

## Slide 12: Risk Driven Design
Focused on risk
What is main risk at start of project?
  Gather requirements at start of project because it is the highest risk area
  Design an architecture because it is the next highest risk
Assess risk and work on riskiest area first

## Slide 13: Risk Driven Development
Driven by technical and business risk
Assess risk
Minimise major risk as quickly as possible
Initial Risks
Initial Project Scope
Define iteration
to address
highest risks
Plan and develop
the iteration
Assess the iteration
Risks
eliminated
Revise risk
assessment
Revise
project plan
Iteration N
(From Quatrani)

## Slide 14: Spiral Development Cycle
Planning
Risk Analysis
Software Dev.
User Evaluation
Initial requirements
gathering and planning
Subsequent planning
following user comment
Initial Risk Analysis
Risk analysis based
on latest plans and
user feedback
Go / No-Go
Decision
Develop first version
or prototype
Subsequent
development or
more prototyping
Initial feedback from
users

## Slide 15: Writing a Space Standard
Requirements
  From many applications
  From many organisations
  From many countries
  Need to build a consensus
Technology
  May not exist
  Target future technologies which may change
  Need to target multiple technologies

## Slide 16: Standards
Terrestrial standards
  Each focused on specific niche
  Has many applications/users within that niche
Space standards
  Limited missions
  Limited applications/users
  Need to cover wide range of applications
  Or it will not be cost effective

## Slide 17: Building the Standards Team
Need an efficient and effective team
Key people
  Systems engineers who have designed missions
  Electronic engineers who have designed flight systems
  A team that will cover the experimentation, prototyping, drafting
  Other teams working on validation
    Applications
    Simulation
    Interoperability

## Slide 18: A Successful Standard
Open standard
  Available for everyone to use
A convincing solution
  With clear benefits
Generic and easily adaptable
  Supporting many applications
IP cores and chips available
  Especially flight capable implementations
International partners
  Proven interoperability
Comprehensible
  Less than 200 pages
  ECSS are a great help

## Slide 19: Testing a Draft Standard
Review against requirements
  To check nothing important missed
High-level software simulation
  To explore alternative solutions
  Focused investigations
VHDL IP Core in FPGA
  Real time execution
  Allows full system testing
Simulation software
  System-C, SDL, OPNET
  Validating standard specification
Interoperability testing
  Is the standard unambiguous and interoperable

## Slide 20: Developing the SpaceFibre Standard
Draft A (Oct 2007)
  Gathering and understanding requirements
  Researching and understanding technologies
  Focused on lower levels of standard
    I.e. the CODEC
  IP core implemented and tested

## Slide 21: Developing the SpaceFibre Standard
Draft B (Sept 2011)
  Introducing QoS and Retry
  Prototyping with software and VHDL
  Drafted in ECSS format
Draft C (Dec 2011)
  Further prototyping and simulation of QoS
  Extensive improvements
Draft D (Feb 2012)
  Formal review
  Validation through simulation
  Interoperability testing
  Corrections and clarifications

## Slide 22: Developing the SpaceFibre Standard
Draft E (Sept 2012)
  Prototype implementation and testing
  Validation through simulation (System-C, SDL)
  Interoperability testing
  Extensive improvements
Draft F (Sept 2013)
  Rationalisation of protocol stack
  Addition of network and management layers
  Improvement of FDIR
  Simplification of lane layer
  Removing of much non-normative material
  Extensive testing in hardware
  First experimental ASIC design

## Slide 23: SpaceFibre Standard
Quality Layer
Lane Layer
VC Interface
Multi-Lane Layer
Physical Layer
Broadcast Interface
Physical Interface
Network Layer
Packet Interface
Management Layer
Management
Interface
Broadcast Message Interface

## Slide 24: SpaceFibre Validation

## Slide 25: Interoperability testing Dec 2012

## Slide 26: SpaceWire-RT
EU Framework 7 research project
Russian and European Partners
Major input to requirements, QoS/FDIR and validation

## Slide 27: SpaceFibre running over 100m fibre

## Slide 28: Conclusions
Development of IP core essential to support standard specification
  Allows full-speed, system-level testing
  Necessary for interoperability testing
  Necessary for demonstration
    Raising confidence in the technology
  Enables early implementations of
    FPGAs
    Test and development equipment
Many iterations of IP core necessary
  For SpaceFibre already many major revisions of SpaceFibre IP core
    Takes a lot of effort
  Complemented by other forms of validation

## Slide 29: Conclusions
Many standards developed in this way:
  SpaceWire
    SpaceWire CODEC and Router cores
  SpaceWire RMAP
    RMAP Target and Initiator cores
  SpaceFibre
    SpaceFibre Interface core
      Including SpaceFibre Lane and QoS
Spiral model an appropriate life cycle model
  Much more appropriate that waterfall or V model