## Slide 1: Current ESA IP-Cores offer and on-going developments
L. Fossati ESA/ESTEC 16/09/2013

## Slide 2: Outline
IP-Cores
  Definition, from a digital point of view
Digital ESA IP-Cores offer
ESA IP-Cores: organization and licensing procedures
ESA IP-Cores: Statistics
Other IP-Cores
  SystemC IP-Cores
  Analog and mixed-signal addressed later

## Slide 3: IP-Cores Definitions
Intellectual Property Core – definition from Wikipedia:
In electronic design a semiconductor intellectual property core, IP core, or IP block is a reusable unit of logic, cell, or chip layout design that is the intellectual property of one party.

## Slide 4: IP-Cores Definitions
Intellectual Property Core – definition from Wikipedia:
In electronic design a semiconductor intellectual property core, IP core, or IP block is a reusable unit of logic, cell, or chip layout design that is the intellectual property of one party.
Legal implications - Intellectual Property (IP) is a legal concept which refers to creations of the mind for which rights are recognized
00100
11100
00010
00101
An IP-Core can be described as being for chip design what a software library is for computer programming

## Slide 5: List of digital ESA IPs
HurriCANe | CAN Controller | ESA projects only
CUC-CTM | CCSDS Unsegmented Code (CUC) & CCSDS Time Manager (CTM) | ESA Member States*
EDAC |  | ESA Member States*
RT53EUR | MIL-STD-1553B Remote Termina Controller | ESA projects only, netlist
LEON2-FT | Sparc V8 microprocessor | ESA projects only
SpaceWire-AMBA | SpaceWire-b CODEC | ESA Member States*
SpaceWire-b | SpaceWire-b CODEC | ESA projects only
SpaceWire-RMAP | SpaceWire-b CODEC + RMAP | ESA projects only
SpaceWire-RMAP SCOC3 | SpaceWire-b CODEC + RMAP | ESA Member States*
AUIP | TC Authentication Unit | ESA projects only
CCIPC | CanOpen Controller | ESA projects only
PDEC | Packet Telecommand Decoder | ESA projects only
PTCD | Packet Telecommand Decoder | ESA projects only
PTME | Packet Telemetry Encoder | ESA Member States*

## Slide 6: ESA VHDL IP-Cores – 1/7
HurriCANe (ESA / Sitael)
Controller Area Network (CAN) compliant with Bosch CAN Protocol 2.0 part A, B
AMBA APB interfaces
Available for the ESA Member States
Missions: ExoMars, Sentinel-1, BepiColombo, Galileo, Columbus, etc.
Components: SCOC3, MDPA, Essential Telemetry ASIC, SpW-RTC
CUC-CTM (ESA)
CCSDS Unsegmented Code (CUC) & CCSDS Time Manager (CTM)
  provides basic time keeping functions (CUC) and additional CCSDS time services (CTM)
AMBA APB Interfaces
Available for the ESA Member States
Missions: Proba-2, Proba-3, Proba-V, BepiColombo, etc.

## Slide 7: ESA VHDL IP-Cores – 2/7
EDAC (ESA)
Simple Error Detection And Correction IP Core
  data widths from 4 to 64 bits, Single Error Correction and Double Error Detection, for some configurations Double Error Correction and Single Bank-error Detection – Hamming / Cyclic codes
Pure combinatorial implementation
Available for the ESA Member States
Missions: BepiColombo, Sentinel-2, Proba-3, AlphaSat, etc.
Components: VASP
LEON2-FT (ESA / Aeroflex Gaisler)
Sparc V8 compliant microprocessor
  Hw multiply and divide units, 5 stage pipeline, L1 cache, FPU support (none included in the IP-Core)
Centered on the AMBA AHB and APB busses
Available for ESA Projects only
Missions: ExoMars, GAIA, BepiColombo, Proba-2, Proba-3, etc.
Components: AT697E/F, AGGA4, MDPA, etc.

## Slide 8: ESA VHDL IP-Cores – 3/7
PDEC (Aeroflex Gaisler)
Packet Telecommand Decoder – CCSDS packet compliant
AMBA AHB interfaces
Available for the ESA Projects only
Missions: BepiColombo, Proba-3, Galileo, SWARM, etc.
Components: SCTMTC, CROME
PTCD (Astrium)
Packet Telecommand Decoder – CCSDS packet compliant
  Soft-core version of the chip MA28140 from GEC-Plessey Semiconductors
AMBA APB and AHB interfaces
Available for the ESA Projects only
Missions: Proba-3, ATV, AlphaBus, SEOSAT
Components: SCOC3

## Slide 9: ESA VHDL IP-Cores – 4/7
PTME (ESA)
Packet Telemetry Encoder
  Compliant with CCSDS and ECSS standards for telemetry and channel coding
AMBA APB Interface
Available for the ESA Member States
Missions: BepiColombo, Proba-2, Proba-3, ATV, SEOSAT, Galileo, etc.
Components: SCTMTC, CROME, Essential Telemetry ASIC
RT53Eur (Astrium)
1553B Remote Terminal
Custom DMA interface to SRAM
Available for ESA Projects only (netlist)
Missions: BepiColombo

## Slide 10: ESA VHDL IP-Cores – 5/7
CCIPC (Sitael)
CANopen Controller
  On top of CAN bus it implements the CANOpen application layer services as defined in CiA (http://www.can-cia.org/ ) standard “CANopen Application Layer and Communication Profile”
  Available also in a “reduced” version for smaller silicon area usage
Various interfaces to the host system (including AMBA AHB and APB)
Available for ESA Projects only
Missions: ExoMars
AUIP (RUAG)
Telecommand Authentication and Encryption
  Includes key management functionality and Logical Authentication Channel
Host interface through dedicated signals (including two memory interfaces)
Available for ESA Projects only
Missions: Sentinel 1, 2, 3

## Slide 11: ESA VHDL IP-Cores – 6/7
SpaceWire-b CODEC (University of Dundee)
Implementation of standard ECSS-E-ST-50-12C
FIFO and Signals for communicating with the host system
Available for ESA Projects only
Missions: BepiColombo, Gaia, JWST, Herschel, Sentinel(s), etc.
Standard components: AT7911E, AT7912F, AGGA4, SCOC3, SpaceWire RTC (AT7913E), SpaceWire Router (AT7910E)
SpaceWire AMBA (Astrium)
Implementation of standard ECSS-E-ST-50-12C
AMBA APB and AHB interfaces
Available for the ESA Member States
Missions: ExoMars, BepiColombo, Proba, MASER, GAIA, etc.

## Slide 12: ESA VHDL IP-Cores – 7/7
SpaceWire-RMAP (University of Dundee)
Implementation of ECSS-E-ST-50-52
AMBA APB and AHB interfaces
Available for ESA Projects only
Missions: ExoMars, BepiColombo, Astro-H
SpaceWire-RMAP SCOC3 (Astrium)
Implementation of ECSS-E-ST-50-52
AMBA APB and AHB interfaces
Available for the ESA Member States
Missions: SEOSAT, SPOT6
Standard components: SCOC3, CWICOM

## Slide 13: SpaceWire IP-Cores - summary
 | Developer | Function | Ifs | Licensing Scope | n. Requests
SpW-b | U. Dundee | SpW CODEC | FIFOs | ESA Projects | 108
SpW AMBA | U. Dundee | SpW CODEC | AMBA/DMA | Member States | 21
SpW-RMAP | Astrium | SpW-CODEC + RMAP | AMBA/DMA | ESA Projects | 63
SpW-RMAP SCOC3 | Astrium | SpW-CODEC + RMAP | AMBA/DMA | Member States | 0

## Slide 14: ESA IP-Cores Service started in 2002
Roles of ESA:
Promote/Manage IP-Core development and re-use
  On-Going Developments (TRP/GSTP/ECI …): CCSDS File Delivery Protocol, SpaceFibre, Mass-Memory Controller & File-System …
Licensing to European (space) Industry
  Processing requests, producing licenses, solving legal issues …
Providing Support (in the context of ESA projects)
  Answering technical issues, Investigations in the Lab …
Centralize IP users’ feedback
IP Maintenance and Updates
  Following users’ feedback on code bugs, documentation gaps or errors
  Through contracts with Industry and internally (lab. activities)
Notes: Talk about the AIM of the IP-Core service at the beginning, so that later-on we can say what ESA does

## Slide 15: ESA IP-Cores Service Licensing Conditions and Procedure
Complete Request Form at page: http://tinyurl.com/ESAIPCores
A License will be produced for signature by ESA and licensee
  A document is attached to the license to formalize the 5000€ handling fee
The requested IP-Core is delivered
  Limited technical support is provided
Each IP-Core has associated its licensing conditions
  e.g. some can only be licensed in the frame of ESA activities
A handling fee of 5000€ is associated to each IP-Core License
  i.e. to each requested IP-Core and for each usage of it
  See http://tinyurl.com/ESAIPCores for more details
  Necessary to sustain the service
In some situations it is possible to obtain licenses for the use in non-ESA projects and, even, by companies not in ESA member states
Notes: Talk about the AIM of the IP-Core service at the beginning, so that later-on we can say what ESA does

## Slide 16: Statistics – 1 Usage in ESA Projects/Programs
Chart: 
| TRP | GSTP | BepiColombo | ExoMars | INFRA | PROBA | Sentinel-1 | Cosmic Vision | Maser | EOEP | ARTES 4 | Greek TF | CTP | ARTES | NPI | Portu. TF | GAIA | ESEO | Sentinel-3 | COLUMBUS | ISS | SEOSAT | AlphaBus | ECI | PECS | LET SME | ARTES 5.2 | Euclid | Czech TF | Sentinel-2 | NPAL | Galileo | ASTRO-H
 | 94 | 45 | 35 | 27 | 23 | 9 | 9 | 8 | 6 | 5 | 5 | 5 | 5 | 5 | 5 | 4 | 4 | 3 | 3 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 17: Statistics – 2 Total Requests per Year
Chart: 
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
 | 14 | 22 | 60 | 64 | 39 | 36 | 39 | 45 | 46 | 34 | 43 | 15

## Slide 18: Statistics – 3 Avg. Requests per IP-Core/year
Chart: 
| SpWb | SpW-AMBA | CAN | LEON2-FT | SpW-RMAP | CCIPC | PTME | EDAC | CUC-CTM | SpW-b-SysC | RT53EUR | IP1553 | AUIP | PTCD | PDEC | IP-Xact LEON2-FT | LEON-SysC
 | 10.6262 | 6.9147 | 6.3072 | 5.3983 | 4.934 | 3.9827 | 3.0848 | 2.2491 | 1.5424 | 1.4977 | 1.3623 | 1.2282 | 0.9972 | 0.93056 | 0.82716 | 0.27247 | 0.27247

## Slide 19: Statistics – 4 Evolution of the Portfolio
Chart: Year
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Number of IPs | 5 | 8 | 13 | 13 | 13 | 13 | 13 | 14 | 18 | 20 | 22 | 23

## Slide 20
Simulatable SystemC IP-Cores
(high-level IP-Cores model)

## Slide 21: Hardware Modeling: Activities

## Slide 22: SoCRocket VP Infrastructure
Hardware Models are not enough to create a Virtual Platform
  The infrastructure to interconnect, manage them and extract results is also needed
Interconnection
Configuration
Power Monitoring
SW Debugging
Performance Monitoring

## Slide 23
Analog IP-Cores
Will be presented later-on in the afternoon’s session

## Slide 24: Thank You for Listening
For more information:
  Luca.Fossati@esa.int
  http://microelectronics.esa.int

## Slide 25: IP-Cores License - 1
5.1 ESA MEMBER/PARTICIPATING STATES. Granted rights are limited to the territory of the Member/Participating States of the European Space Agency. Should Licensee wish to manufacture, have manufactured or sell any product derived from the HDL IP-Core outside this territory, he shall submit a written notice to Licensor for information indicating the terms proposed for the licence. Such a request can be submitted to and agreed by ESA at the same time as signing the licence agreement.
In principle use restricted to the ESA member/participating states; to use the IP-Core and any derivatives (i.e. even a unit containing an ASIC which instantiated the IP-Core) a special request has to be submitted to the Agency Technology Transfer Board (ATB)

## Slide 26: IP-Cores License - 2
6.1 GENERAL SCOPE. Licensor hereby grants Licensee a non-exclusive, non-transferable right to instantiate the synthesizable HDL IP-Core into integrated circuits, to manufacture, have manufactured and use such integrated circuits or else to incorporate such integrated circuits in hardware or equipment only in the legal frame work of the ESA Project “<ESA PROJECT NAME HERE> AND/OR ESTEC/ <contract number>”.
When a license is granted in the frame of an ESA project (note that some IP-Cores can only be license in this context) use of the IP-Core or of any derivative is forbidden outiside the legal framework of such project (e.g. if an ASIC is developed in a GSTP activity, to commercialize it another license must be obtained, either from ESA or from the IP-Core owner)

## Slide 27: IP-Cores License - 3
7.4 GENERAL UNDERTAKINGS BY LICENSOR / TASKS EXPLICITLY EXCLUDED: Licensor shall report to Licensee all design and/or documentation errors which are found by, or become known to, Licensor and shall provide Licensee with the corresponding replacements of, or additions to, the relevant file(s) listed in Annex A hereto, if and when available. It is specifically understood that any replacement of, or addition to, the files listed in Annex A hereto issued to Licensee by Licensor shall be subject to the terms and conditions of this licence.
Seldom applied, please report to us your experience using the IP-Cores, it helps improving the quality of the offer, for your and other’s future use.

## Slide 28: IP-Cores License - 4
11.1 NO WARRANTY ON IP-CORES. Licensor gives no warranty nor guarantee whatsoever as to the adequacy or suitability of the licensed synthesizable HDL IP-Cores and shall not be held liable for any direct, indirect nor consequential damages. Use of the licensed synthesizable HDL IP-Cores by Licensee is made fully at Licensee’s own risk.
We try to the best of our possibilities to provide technical support either directly or through subcontracts with the original developer of the IP-Core. Unfortunately due to the limited resources allocated to the ESA IP-Cores service, we cannot take any a-priori commitment.

## Slide 29: IP-Cores License - 5
8.1 CREATION OF CORRECTIONS TO THE IP-CORES.
8.2 CREATION OF MODIFICATIONS TO THE IP-CORES.
8.3 CREATION OF ADDITIONS TO THE MODELS.
Depending on the IP-Core, modifications may either belong to the licensee or to the owner of the IP. Corrections always belong to the owner of the IP and additions always to the licensee.