## Slide 1: RAD HARD ASICS FOR COSMIC VISION MIXED SIGNAL IPS INTEGRATION F. Gutiérrez (ARQUIMEA) D. González (ARQUIMEA) R. Jansen (ESA)
High Frequency Reconfigurable
ASIC for Cosmic Vision
RUN1
(Test Chip with all analog blocks)

## Slide 2: OUTLINE
ABOUT ARQUIMEA
SCOPE OF THE PRESENTATION
BACKGROUND
THE RECONFIGURABLE ASICS FOR COSMIC VISION
IPS DESIGN AND INTEGRATION EXPERIENCE
IPS DEVELOPMENT ROADMAP
OPEN QUESTIONS
CONCLUSIONS

## Slide 3: ABOUT ARQUIMEA
MAIN CUSTOMERS & PARTNERS
MICROELECTRONICS
MECHANICAL ACTUATORS
SPACE SCIENCE (SENSORS & ROBOTIC PARTS)
ITAR FREE / FABLESS /SPACE FOCUSED

## Slide 4
ABOUT ARQUIMEA
CAPABILITIES IN MICROELECTRONICS
DESIGN
DESIGN VERIFICATION
RADIATION SIMULATION
ASSEMBLY
PACKAGE SELECTION
RELIABILITY
TESTING & QUALIFIC.
ELECTRICAL TEST & ESD
ENVIRONMEN-TAL TEST
MECHANICAL TEST
RELIABILITY TEST
RADIATION TEST
RAD HARD ANALOGUE
RAD HARD MIXED SIGNAL
TEST VEHICLES
FPGA to ASIC CONVERISON
FEASIBILITY ANALYIS
ASIC DEVELOPMENT PLAN
MANUFACTU-RING
TECHNOLOGY HARDENING BY DESIGN
LIBRARIES & DK MODIFICATION FOR RAD HARDENING
MPW
MLM
FULL MASK
RAD HARD DIGITAL
RADIATION TEST SET-UP DEVELOPMENT.
FUNCTIONAL
COLLABORATORS UC3M (ESP), UPM (ESP), USE (ESP)
TECHNOLOGIES IHP (SGB25RH), ON SEMI (I3T80), UMC 180nm/DARE (IMEC), UMC 90nm (ATMEL), ….
ASSEMBLY HOUSES MICROSS, HCM
TEST HOUSES ALTER TUV NORD, INTA
PACKAGE DESIGN
SPEC REVIEW
TECHNOLOGY SELECTION
COLLABORATORS IMEC (BE), UC3M (ESP), UPM (ESP), UIB (ESP) USE (ESP), UPC (ESP). CNM (ESP), SOFICS (BE) , IDM+ (RU), MINDCET (Be)
RH MIXED SIGNAL ASICS DEVELOPMENT AND PROCUREMENT
SPACE RH STANDARD PRODUCTS DEVELOPMENT
FULL SUPPLY CHAIN MANAGEMENT
RH IP’s DESIGN

## Slide 5: SCOPE OF THE PRESENTATION
WE PRESENT :
THE WORK IN PROGRESS IN THE DEVELOPMENT OF TWO RECONFIGURABLE ASICS FOR COSMIC VISION
THE EXPERIENCE IN IPS INTEGRATION IN THE FRAME OF COSMICS VISION ASICS DEVELOPMENT.
THE ROADMAP AND THOUGHTS TO MAKE THE ANALOG MODULES INCLUDED IN THESE ASICS AS IPS REUSABLE IN ESA PROGRAMMES.
THE OPEN QUESTIONS CONCERNING ANALOG IPS BUSINESS MODEL AND INTEGRATION FLOW.
WE EXPECT:
TO GET FEEDBACK FROM POTENTIAL
USERS ABOUT THE REQUIREMENTS TO
REUSE THESE IPS
TO GET FEEDBACK FROM OTHER INTEGRATORS OF MIXED SIGNAL ASICS BASED ON UMC180/DARE.

## Slide 6: BACKGROUND
TODAY’S ARQUIMEA BUSINESS STRATEGY IS ORIENTED TO MIXED SIGNAL ASICS DEVELOPMENT.
ARQUIMEA IS LEADING A CONSORTIUM TO DEVELOP TWO RECONFIGURABLE ASICS FOR COSMIC VISION UNDER TWO ESA CONTRACTS.
THE ANALOG BLOCKS THAT FORM PART OF THESE ASICS COULD POTENTIALLY BECOME REUSABLE IPS.
The commercialisation of IPs or the orientation towards the IP business is still under analysis.
ARQUIMEA is responsible of the integration of several Mixed Signal blocks in single chips (one chip per project).
 ARQUIMEA is analysing in detail the actions to be taken to offer this IPs for ESA projects with the maximum warranties.

## Slide 7: THE RECONFIGURABLE ASICS FOR COSMIC VISION
TWO RECONFIGURABLE RAD TOLERANT ASICS ARE BEING DEVELOPED:
MF ASIC: 0.1 to 10 MHz
HF ASIC: 10 to 100 MHz
  Radiation tolerant (300 Krad(Si))
    Aspect ratio (W/L)>2
    Guard rings
    Isolation in pockets…
  Reconfigurable
  Tunable
  Multi-functional
  Suitable for multiple
  instrumentation applications.
TECNOLOGY: UMC 180nm CMOS & DARE LIBRARY
+ DARE LIBRARY

## Slide 8: THE RECONFIGURABLE ASICS FOR COSMIC VISION
The ASICS are conceived to suit at least the following applications:
  ADC
  DAC
  Filter
  Low Noise Amplifier
  Power Amplifier
  Bessel Filter
High Frequency Reconfigurable ASIC
RUN1
Test chip
Layout view

## Slide 9: THE RECONFIGURABLE ASICS FOR COSMIC VISION DESIGN TEAM
IMB-CNM (CSIC) F. Serra (ICAS) | Analog Design of ADC and DAC MF ASIC
IMSE –CNM (CSIC) G. Leger | Analog Design of ADC and DAC HF ASIC
UPC J. Madrenas (AHA) | Analog Design of LNA and PA
UC3M L. Entrena/M. García | Digital design for all blocks
ARQUIMEA (Design team) | Common blocks and chip integration
USE * A. Torralba/F. Muñoz | Design of Filters
IMEC* | Digital Backend (DARE Library)
* External service

## Slide 10: THE RECONFIGURABLE ASICS FOR COSMIC VISION IPS SPECS…
Medium frequency ASIC (100KHz/10MHz)
Blocks | Spec
ADC | 17 ENOB@ 0.1 MHz – 2 mA 12 ENOB@ 10 MHz – 20 mA
DAC | 17 bits (effective)@ 0.1 MHz – 2 mA 12 bits (effective)@ 10 MHz – 20 mA
Low Noise Amp. | [-6 ; 30] dB Gain in Voltage Mode – 24 mA max 8.5 nV/√Hz Noise density @ 1 MHz [3 ; 3000] kΩ Gain in Current Mode – 24mA max. 518 fA/√Hz Noise density @ 1MHz and 3MΩ gain
Bessel Filter | Bandwidth 0.05 to 5 MHZ – 0.05 to 2 mA
Power Amp | Voltage (160 mA max) THD -74dB @ 1 MHz Current mode (120 mA max) THD -63dB @ 1 MHz
Common blocks | Power-on-reset, Bandgap (1.25V+-5mV), Voltage regulators (3.3 to 1.8V)

## Slide 11: THE RECONFIGURABLE ASICS FOR COSMIC VISION …IPS SPECS
High frequency ASIC (10MHz/100MHz)
Blocks | Spec
ADC | 12 ENOB@ 10 MHz 10 ENOB@ 100 MHz – 250 mA
DAC | 12 bits (effective)@ 10 MHz 9 bits (effective)@ 100 MHz – 60 mA
Low Noise Amp. | [-6 ; 30] dB Gain in Voltage Mode – 49 mA max 4.4 nV/√Hz Noise density @ 10 MHz [3 ; 3000] kΩ Gain in Current Mode – 49mA max 8.8pA/√Hz Noise density @ 10MHz and 3kΩ gain
Bessel Filter | Bandwidth 5 to 50 MHZ – 8.5 mA
Power Amp | Voltage (120 mA) THD -66dB@ 10MHz Current mode (120 mA max) THD -47db @ 10MHz
Common Blocks | Power-on-reset, Bandgap (1.25V+-5mV), Voltage regulators (3.3 to 1.8V)

## Slide 12: THE RECONFIGURABLE ASICS FOR COSMIC VISION STATUS…
BLOCK DESCRIPTION | STATUS (RUN 1, TEST CHIP)
15 bit ADC | First silicon available Preliminary test ongoing Test to be completed Q4 2013
15 bit DAC | 
Low Noise Amp. | 
Bessel Filter | 
Power Amp | 
Common Blocks | 
High frequency ASIC (10MHz/100MHz)
Test Chip basic preliminary testing ongoing.
(Startup, configuration, accessibility and life check on all IPs)
Radiation test after electrical characterization will be performed in separate project.

## Slide 13: THE RECONFIGURABLE ASICS FOR COSMIC VISION …STATUS
BLOCK DESCRIPTION | STATUS (RUN 1, TEST CHIP)
19 bit ADC | Layout ongoing
19 bit DAC | Layout ongoing
Low Noise Amp. | Design complete (waiting for integration and silicon)
Bessel Filter | Layout ongoing
Power Amp | Design completed (waiting for integration and silicon)
Common blocks | Design complete (waiting for integration and silicon)
Medium frequency ASIC (100KHz/1MHz)
Complete Test Chip will be taped-out at the beginning of 2014
Radiation test after electrical characterization will be performed in separate project.

## Slide 14: THE RECONFIGURABLE ASICS FOR COSMIC VISION IPs REUSABILITY
The MS blocks (IPs):
Are valid only for UMC 180 µm CMOS technology and DARE LIBRARY.
 May require re-design if technology changes occur during IC implementation.
 IP integration may require support from the IP designer/generator (via ARQUIMEA).
The MS blocks (IPs) will be able to be:
  DIRECTLY re-used to build other ASICs
  TUNED or modified to meet customer needs.
The MS blocks (IPs):
Are configurable and therefore can meet a wider range of applications than expected from ordinary IPs!
This configurability is expected to limit the need for adaption of future customers!
Notes: Mention the different gains of the amplifier, single ended/differential voltage/current input or the range of operating frequencies of the ADC and appropriately changing SNR in the case of the MF ADC/DAC

## Slide 15: THE RECONFIGURABLE ASICS FOR COSMIC VISION …HF TEST CHIP IPS AND FLOORPLANT…
The MS blocks are meant to be connected externally/ internally to realise an analog processing chain
A complete set of IP blocks for analog signal amplification/conditioning for high performance analog signal processing have been implemented (in the 100kHz to 10MHz and 10MHz to 100MHz range).

## Slide 16: THE RECONFIGURABLE ASICS FOR COSMIC VISION HF TEST CHIP IPS AND FLOORPLANT

## Slide 17: IPS DESIGN AND INTEGRATION EXPERIENCE DESIGN
  IPs design has been performed by individual design groups coordinated by ARQUIMEA.
  Each design group developed only the analog part of each corresponding block.
  One group was in charge of all the digital configuration of the chip and also the digital side of the HF ADC, the HF DAC and the MF DAC implementation.
  The reusable IPs are then MS and consist of an analog and a digital part which have been provided by different design groups.
  DESIGN EXPERIENCE HIGHLIGHTS
  The split of the digital and analog parts of the converters design between two different groups required extra coordination and simulation effort.
  Same configuration interface (SPI) for all the IPs is a great advantage in terms of reusability and testability.

## Slide 18: IPS DESIGN AND INTEGRATION EXPERIENCE VERIFICATION
Verification included four levels:
  Analog verification done by each analog block design team.
  Digital verification by the digital design team
  MS verification per block, by each analog block design team
  Chip level verification (interconnection and routing) by ARQUIMEA.
.
VERIFICATION EXPERIENCE HIGHLIGHTS
Chip level verification quite challenging due to the complexity related to the multiple blocks included in the ASIC.
LVS with Black boxes not straight forward the first time you face it.
Top LVS (layout vs schematics) check done by ARQUIMEA with black boxes on the digital blocks.
Complete top level LVS check done by IMEC.

## Slide 19: IPS DESIGN AND INTEGRATION EXPERIENCE TEST
  Test activities in the project include three levels:
    Individual IPs (on the test chip).
    Full chip (on the final chip)
    System (on the final chip)
    (Test Chips and final ASICs will be radiation tested in the frame of a parallel project)
Test philosophy at IP level will consist of three steps:
  Preliminary test to check if the IPs are alive.
  Performance validation for selected frequencies /configurations + functional test for the rest of frequencies/configurations.
  Full performance validation before IPS are made public.
.
TEST EXPERIENCE HIGHLIGHTS
The resolution, noise and distortion requirements of the IPs are very demanding in terms of test equipment and setup.
The multitude of configurations for the IP requires a special test approach.

## Slide 20: IPS DESIGN AND INTEGRATION EXPERIENCE INTEGRATION…
  The integration of the chip has required:
    Integration of different blocks from different design teams required careful interfaces definition and coordination (for analog to digital interfaces).
    Active interaction with IMEC for a correct digital layout constrains and layout abstracts insertion.
  INTEGRATION EXPERIENCE HIGHLIGHTS
  Special integration flows were required due to the use of DARE library for the digital part and IO pads (see integration phases and charts in next slides).....

## Slide 21: IPS DESIGN AND INTEGRATION EXPERIENCE …INTEGRATION…
  INTEGRATION PHASES description:
Detail design
  The IP has to be integrated in the ASIC at layout level.
Preliminary design
  The IP has to be integrated in the ASIC at schematic level.
    Analysis/IP selection
      Departing from IPs datasheet, high level models and simulations the integrator will analyse if the IP meets the ASIC requirements (functional, area, electrical performance and interfaces).

## Slide 22: IPS DESIGN AND INTEGRATION EXPERIENCE ….INTEGRATION… Integration flow experience…

## Slide 23: IPS DESIGN AND INTEGRATION EXPERIENCE …INTEGRATION… …Integration flow experience…

## Slide 24: …IPS DESIGN AND INTEGRATION EXPERIENCE …INTEGRATION …Integration flow experience

## Slide 25: IPS DEVELOPMENT ROADMAP HF ASIC and IPS: 10 to 100 MHz
The ultimate goal is to qualify a product with these IPs that could be used to assure its quality.

## Slide 26: IPS DEVELOPMENT ROADMAP
MF ASIC and IPS: 0.1 to 10 MHz
The ultimate goal is to qualify a product with these IPs that could be used to assure its quality.

## Slide 27: OPEN QUESTIONS
Test versus warranties (liability versus datasheet and test data......)
Responsibilities in case of failure will depend on the root cause (IP bugs, wrong or improper integration, IP used put of spec, wrong interface, technology changes....)
Documentation, tools and simulation models to be homogenised for ESA analog/MS IPs(?)
.....

## Slide 28: CONCLUSIONS
ARQUIMEA’s experience in the development and integration of mixed signal blocks in the frame of two reconfigurable ASICS developed for COSMIC VISION has been provided.
Integration flow for the mixed signal ASICS with DARE library requires the definition of specific protocols to be followed. The ARQUIMEA experience is provided to be positively exploited.
Set of questions has been left open for further discussion.

## Slide 29
Thank you for your attention!
...any questions...?
fgutierrez@arquimea.com
+34 627495410