## Slide 1: Advanced CCSDS File Delivery Protocol Hardware IP Core
Sören Michalik, Rolf Meyer, 16th September 2013
Notes: Names
Department Chip Design for Embedded Computing of University of Braunschweig
As a contractor we are developing a HW-IP Core implementing the CCSDS File Delivery Protocol for the European Space Agency
Today: -> Overview of current development status
-> Overview of the IP architecture
-> Show some results of first Evaluation tests

## Slide 2: The CCSDS File Delivery Protocol (CFDP)
Delay tolerant File Delivery Protocol for Space
Configuration parameters to adapt communication
(distance in light-time, timer limits, IDs …)
Reliable file transfer and remote file system
management over interplanetary distances
Features
Unreliable and reliable sender
Delivery of files and user messages
Reliability: CRC / File Checksum
maximum 64kB packet size, 4GB file size
Notes: - Delay tolerant File Delivery protocol standard of the CCSDS
Standard from Consultative Committee for Space Data Systems
- Specifically designed for space missions
-> enhanced configurability for space applications
Example: Local Entity: GROUND
Remote entity = SAT
-> protocol allows to configure distance->light time, timer_values, timeouts limits)
-> allows to do reliable file transfer and remote file system management over interplanetary distances
In this study
-> Unreliable and reliable transfers services -> class 1, class 2 sender
-> Delivery of files AND user messages -> Protocol Data Unit -> PDU
-> Reliability Features -> CRC, File Checksum
-> Configurable Maximum Packetsize of up to sixty_four(64)kB , configurable filesize of maximum four(4)GB

## Slide 3: External requirements driving the Architecture
Variability
Performance
ESA Euclid Mission
  850Gbit/Day
  75Mbit/s downlink
High Configurability
Different CCSDS encapsulation formats
Generic Filestore Interface
CAD Tool & commercial library independence
Next Generation Mass Memory
  Average 1.5Gbit/s
  Maximum 5Gbit/s
Notes: Various requirements driving implementation in HW-IP
Performance requirements
-> upcoming missions
-> euclid / unit gathering 850Gbit/day,
-> transferring with 75Mbit/s when in contact with ground station
-> high datarate required
-> development shows that we will have faster memories in space missions
-> Next generation MM -> also maximum data rate of 5 Gbit/s
Variability requirements
-> High Configurablity
-> Different CCSDS encapsulation formats
-> generic filestore IF
-> independent from libraries and Tools
-> IP HW architecture fullfills all needs of future space missions

## Slide 4: Workflow of the Study
  Features Selection
  Hardware/Software Partitioning
IP Core Definition
  IP-Hardware modeled in SystemC
  Tests on SoCRocket Virtual Platform
SystemC IP Core Implementation
  VHDL - Hardware design based on SystemC models
  SEE Mitigation and LEON2FT System integration
VHDL IP Core Implementation
  Map to a RASTA compatible FPGA prototyping board
  Tests
IP Core Validation and Deployment
  Map to FPGA technologies
Technology Mapping
Current Progress
Notes: IP Core Definition -> Feature selection / HW-SW partitoning
SystemC IP Core Implementation
-> SysC implementation, Tests on SocRocket
VHDL IP Core Implementation
-> VHDL model implementation based on SysC models
Validation and Deployment
Technology Mapping
Project state 2/3 of development
Project will be finished by April next Year

## Slide 5: CFDP-IP System Architecture
CFDP RTEMS
Software
Management Information Base
Encapsulation
Service
PDU
Serializer/
Deserializer
CFDP
IP Core
LEON2FT Processor
Communication Interface
Transaction Manager
Transaction Processor
Class1
Class2
Context
Configuration
Packet Data
File Store
Configuration
File Data
Control
Packet Data
Notes: - Designed as Co-Processor -> Leon2FT
- HW-SW part -> RTEMS Software
Software Configures and controls IP -> starts new TA for example
Interface for requesting filedata from filestore
Link to the Communication IF or a memory region to send/receive packets
IP Consists of 5 HW models
MIB
Heart -> TM + TP
Transaction Processor -> Statemachines Class1 Class2
Transaction Manager -> TA Scheduling,
-> since multiple active TA at a time
PDU Ser/Deser -> PDU creation
- Encapsulation Service -> PDU Encapsulation in CCSDS Packet Encapsulation formats
Deeper look in PDU serialization process ->

## Slide 6: PDU Serialization/Deserialization Pipeline
PDU Serializer
PDU Deserializer
AHB
AHB
Encapsulation Service
Unitdata Transfer Interface
Transaction
Processor
Transaction
Manager
High throughput of processing pipeline:
up to 1Word/cycle  400 MB/s @ 100MHz
ACK
Filedata
EOF
Metadata
NACK
Finished
ACK
Encapsulation
Packet
Raw PDU
Space
Packet
TX FIFO
RX FIFO
CRC
CRC
Data out
Response in
Notes: Overview of PDU Ser/Deser Process -> from generation to transfer to commuication inteface
Start at TP -> example filedata PDU
Serializer, CRC
Encapsulation Service -> PDU Encapsualtion
Unitdata transfer -> FIFOs + AHB Communication ->Memory or Communication Interface
Receiver other direction -> decapulation, Deserialization -> TM
All components modeled in HW -> Very good Performance due to HW implementation
About 1 Word/ per cycle (best utilization)
-> 400MB/s throughput

## Slide 7: SystemC IP Development
Early software and driver development
Evaluation of SystemC-IP architecture and
interface configuration during the development
Measuring performance
Modeled in SoC-Rocket virtual processor platform
Design Space Exploration
Find an optimal configuration of the IP-Core architecture and interfaces to improve the maximum performance
Notes: - To implement this IP we started in the previous phase with SystemC model Dev
- Allows Early software and driver development
Able to Evaluate IP architecture + interface configuration
Measure performance
Modeled sysC components using SocRocket Virtual Processor Platform -> developed at our department
Used this platform for DSE
-> find the best configuration of Architecture Interfaces -> improve performance
To show more details about the SocRocket Platform -> Rolf (involved in development of SoCRocket )

## Slide 8: The SoCRocket Virtual Platform SystemC/TLM2 Simulation IP + Design Infrastructure
Models provided by ESA (integration only)
AHB2SW
AHBCTRL
LEON ISS
Caches, MMU,
localrams
MCTRL
SRAM
SoCWire
GPTimer
SpaceWire
IRQMP
AHB2APB
AHBMEM
APB UART
CFDP
SDRAM
IO
PROM
Simulation model for GRLIB core components
Models featuring different operating point:
  Extensive Design Space Exploration (high accuracy / medium speed)
  Low-Level SW Development & Early Exploration (medium accuracy / high speed)
new model
Notes: The SoCRocket Platform is a SystemC/TLM2 Virtual Machine which consists of models of all major components of the Aeroflex Gaisler GRLib.
The ESA Provided us the LEON ISS and SpaceWire TLM Model and we’ve written the other models by our self:
GPTimer, IRQMP, APBUart, AHB2APB Bridge AHBMem MCtrl, and a generic memory model as well as a AHBCtrl model with PnP support and a full Sparv V8 MMU_Cache with localrams.
The VP is mainly used in 2 different scenarios:
In Design-Space-Explorations in loosely timed mode: High Accuracy but therefore not as fast. Only 100 times faster than RTL Co-Simulation.
And for low-level SW Development and early exploration with less accuracy but faster. Over 5000 times faster than RTL Co-Simulation.
In phase two we’ve build a CFDP SystemC model which we used in early exploration mode to optimize our design.

## Slide 9: SoCRocket – Example use cases and features
HW IP Development:
Infrastructure for quickly building new components e.g. Bus-Interfaces, Register Container inherited from library base-classes
Integration of RTL components with custom transactors
Low-Level SW Development:
Register/bit true system environment
SW Flow equivalent to GRLIB: including boot code
Support for real-time OS: RTEMS, µC OS, …
System Exploration:
Runtime reconf. – all parameters can be change without compilation
Lots of debugging and analysis features
Notes: To do so SoCRocket is not only a collection of models.
The models are build on a strong foundation.
We’ve created Infrastructure to support the construction of new models and transactores to verify their behavior and timing agains actual RTL IP.
For Software Development we present a Bit true system. All registers are behaving exactly like in RTL.
You can use the same software flow. Precompiled executables can be run and we support the same bootcode as a equivalent GRLib Design.
Moreover we have support for real-time OSes in CFDP we’ve written a driver in RTEMS on the VP.
Different types of VP can be configured in an easy manner by using a GUI configuration Wizard and the configuration can easiely be changed at runtime without recompilation.
Furthermore the VP has extensive debugging mode with gdb support in both Hardware model and Software to see exactly whats going on.
Which actually was very useful while writing the software and to identify the bottelneck in the CFDP IP.

## Slide 10: Design Space Exploration - Baseline System Architecture
APB
AHB
mst
PDU
Serializer/
Deserializer
CFDP
IP Core
CFDP RTEMS Software
Memory
(+Emulated Filestore)
CFDP
Driver
CFDP
Runtime
CFDP
Client
LEON2FT Processor
Ethernet/
Spacewire
CRC Engine
AHB
All Masters access the same bus / memory Bottleneck!
MIB Registers
MIB
Encapsulation
Service
Unitdata Registers
Primitives Registers
Transaction Manager
Transaction Processor
S1
S2
Context
Filestore Registers
Unitdata IF
Filestore IF
IRQ
Notes: We used this Platform for the DSE
Baseline Arcitecture
5 IP models connected to AHB interface
-> system bus
-> filestore is implemented in SW for this configuration
-> basic configuration
During Transaction
-> Transaction Processor receives file segement data from filestore,
-> while Encapulation service produces outgoing PDU data
Discovered Bottleneck!
-> Master Interfaces ,same AHB bus, same memory -> leads to bottleneck

## Slide 11: CFDP - Performance Analysis (baseline architecture)
Transaction Processor and
Encapsulation Service
access AHB (Memory)
in parallel / in turns
Arbitration overhead
The maximum throughput
is limited by the speed of
the external memory
(~33MB/s in simulation)
 Bottleneck !
Chart: time(µs)
Single File Transfer (1MB) using 64kB Segments
Notes: Plot of throughput for these 2 interfaces
-> throughput over time for a single file transfer
-> TP + ES access AHB in turns / parallel
-> In addition ,Throughput is limited by external memory
-> Bottleneck!
Even worse if other processor loads accessing the AHB system bus / memory

## Slide 12: CFDP-IP Enhanced System Architecture
MIB Registers
MIB
Encapsulation
Service
PDU
Serializer/
Deserializer
CFDP
IP Core
CFDP RTEMS Software
Memory
(+Emulated Filestore)
CFDP
Driver
CFDP
Runtime
CFDP
Client
LEON2FT Processor
Ethernet/
Spacewire
Unitdata Registers
Unitdata IF
CRC Engine
AHB
APB
IRQ
Primitives Registers
Transaction Manager
Transaction Processor
S1
S2
Context
Filestore Registers
Filestore IF
AHB
Mst
AHB
Slv
AHB
RxSlv
AHB
TxMst
Notes: Strictly Separated Interfaces configuration
-> Master for outgoing data
-> Slave for incoming data
As you can see
-> Same configuration as in baseline possible, small changes
-> No performance benefit in this config, but still most generic solution
But this IF configurations allows also to be used like this…

## Slide 13: CFDP-IP Enhanced System Architecture (streaming config)
MIB Registers
Primitives Registers
APB
IRQ
MIB
Transaction Manager
Transaction Processor
Encapsulation
Service
PDU
Serializer/
Deserializer
CFDP
IP Core
CFDP RTEMS Software
Memory
CFDP
Driver
CFDP
Runtime
CFDP
Client
S1
S2
Context
LEON2FT Processor
Ethernet/
Spacewire
Filestore Registers
Filestore IF
CRC Engine
Filestore
Sensor
Data
AHB1
Control
AHB2
Slv
Mst
Unitdata Registers
Unitdata IF
AHB4
AHB3
AHB
Mst
AHB
Slv
AHB
RxSlv
AHB
TxMst
Notes: Configuration with separate busses for each interface
For example: Direct connection to communication module
-> much higher datarates
And: Direct connection to FS
->Filestore can directly stream data to IP Core due to slave IF
In this configuration
-> ommit data exchange through system memory
-> HW filestore support -> streaming
-> system bus completly separated
This Ideal/ best scenario with best performance
-> mixture of interface configuration possible

## Slide 14: Summary
Enhanced System Architecture
AHB Master interface for outgoing (TX) data stream
AHB Slave interface for incoming (RX) data stream
AHB Slave Filestore interface
Benefits
increased system performance
   reduced memory accesses
   direct interface option
   maximum AHB throughput: 3,2Gbit/s = 400MB/s @ 100MHz
enhanced compatibility with HW-filestore implementations
CFDP
IP Core
Notes: Conclusion: We Developed CFDP IP as High Performance IP core
-> good configurability
-> can be used in various enviroments system
We Proposed Enhanced System architecture with separated IF
-> Master outgoing
-> Slave incoming
Benefits
->increased Performance
-> compatibility with HW-FS
Schedule
-> Project will be finished by 15th of april next year
Thank you for your attention!

## Slide 15: Detail: Unitdata Transfer Interface
Encapsulation
Service
Ethernet/
Spacewire
AHB
RxSlv
AHB
TxMst
AHB
Slv
AHB
Mst
Unitdata Registers
Unitdata IF
AHB2
Encapsulation
Service
Ethernet/
Spacewire
AHB
Mst
AHB
Mst
Unitdata Registers
Unitdata IF
Memory
AHB1
AHB3
Memory
Leon
Leon
AHB1
Baseline Configuration:
Enhanced Configuration:

## Slide 16: Detail: Filestore Request
  1. Transaction Processor requests files from filestore (APB)
    Request registers: file_handle
    seek location (pos in file)
    length
  2. Filestore / Leon3 streams filedata
  to Transaction Processor (AHB)
APB
Transaction Processor
CFDP RTEMS Software
Memory
CFDP
Driver
CFDP
Runtime
CFDP
Client
S1
S2
Filestore Registers
Filestore IF
AHB
slv
Control
AHB1
AHB2
AHB
mst
File-
store